## Slide 1
Electronic Devices
Reference book:
Electronic Devices and Circuit Theory (Chapter-2)
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Mid Term Lecture - 04
Faculty Name: Dr. Mohammad Alif Arman
Email : dr.alifarman@aiub.edu
Room: DN0526

## Slide 2
Understand the process of rectification to establish a dc level from a sinusoidal ac input.
Objectives

## Slide 3: SINUSOIDAL INPUTS; HALF-WAVE

## Slide 4: HALF-WAVE RECTIFICATION
The process of removing one-half the input signal to establish a dc level is called halfwave rectification.
The effect of using a silicon diode with VK = 0.7 V is demonstrated in below Figure for the forward-bias region. The applied signal must now be at least 0.7 V before the diode can turn “on.”

## Slide 5: HALF-WAVE RECTIFICATION

## Slide 6: HALF-WAVE RECTIFICATION

## Slide 7: PIV (PRV)
It is the voltage rating that must not be exceeded in the reverse-bias region or the diode will enter the Zener avalanche region.
Applying Kirchhoff’s voltage law, it is fairly obvious that the PIV rating of the diode must equal or exceed the peak value of the applied voltage.

## Slide 8: FULL-WAVE RECTIFICATION: BRIDGE NETWORK

## Slide 9: BRIDGE NETWORK

## Slide 10: BRIDGE NETWORK

## Slide 11: CENTER-TAPPED TRANSFORMER
Network conditions for the positive region of vi

## Slide 12: CENTER-TAPPED TRANSFORMER
Network conditions for the negative region of vi

## Slide 14
Thank You