## Slide 1
Electronic Devices
Reference book:
Electronic Devices and Circuit Theory (Chapter-3)
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Mid Term Lecture - 07
Faculty Name: Dr. Mohammad Alif Arman
Email : dr.alifarman@aiub.edu
Room: DN0526

## Slide 2
P
N
P
Collector
Emitter
Base
The term bipolar indicates that, both electrons and holes contributes to the flow of current.
Three doped regions. The Emitter, the Base and the Collector.
Based on the doping of these three regions, it is known as either NPN or PNP transistor.
There are two PN junctions.

## Slide 3
P
N
P
Collector
Emitter
Base
HOLES
ELECTORNS

## Slide 4
P
N
P
Collector
Emitter
Base
Emitter Heavily Doped
Base Lightly Doped and Very Thin
Collector Moderately Doped
In case of the NPN transistor, the current will flow from the Base towards the Emitter.
PNP transistor, then the current will flow from the Emitter towards the Base region.
B
E
C
N
P
N
P
N
P
B
E
C

## Slide 5: TRANSISTOR OPERATION
The basic operation will be described using the p-n-p transistor.
The operation of the n-p-n transistor is exactly the same if the roles played by the electron and hole are interchanged.
One p-n junction of a transistor is reverse-biased, whereas the other is forward-biased.

## Slide 6: TRANSISTOR OPERATION
Both biasing potentials have been applied to a p-n-p transistor and resulting majority and minority carrier flows indicated.
Majority carriers (+) will diffuse across the forward-biased p-n junction into the n-type material.
A very small number of carriers (+) will go through n-type material to the base terminal. Resulting IB is typically in order of microamperes.
The large number of majority carriers will diffuse across the reverse-biased junction into the p-type material connected to the collector terminal.

## Slide 7: TRANSISTOR OPERATION
Majority carriers can cross the reverse-biased junction because the injected majority carriers will appear as minority carriers in the n-type material.
Applying KCL to the transistor :
The collector current comprises of two components – the majority and minority carriers
ICO = IC current with emitter terminal open and is called leakage current.

## Slide 8: Different Region of OPERATION
Active
Region
Reverse
Active Region
Saturation Region
Cutoff Region
P
N
P
Collector
Emitter
Base
Forward
Reverse
VE
VC
VB
IE
IC
IB
P
N
P
Collector
Emitter
Base
Forward
VE
VC
VB
IE
IC
IB
Forward
P
N
P
Collector
Emitter
Base
Reverse
VE
VC
VB
Reverse
P
N
P
Collector
Emitter
Base
Reverse
Forward
VE
VC
VB
IE
IC
IB

## Slide 9: BJT CONFIGURATION
Output
B
E
C
Input
Common Emitter
Common Base
Common Collector
Output
B
E
C
Input
Input
E
B
C
Output

## Slide 10: COMMON-BASE CONFIGURATION
Common-base terminology is derived from the fact that the :
- base is common to both input and output of the configuration.
- base is usually the terminal closest to or at ground potential.
All current directions will refer to conventional (hole) flow and the arrows in all electronic symbols have a direction defined by this convention.
Note that the applied biasing (voltage sources) are such as to establish current in the direction indicated for each branch.

## Slide 11: COMMON-BASE CONFIGURATION
The free electrons which are flowing from emitter to base.
The holes which are flowing from base to emitter. The width of the base region is very thin. A small percentage of free electrons from emitter region will combine with the holes in the base region and the remaining large number of free electrons enters to the collector region.
Free electrons of the collector region will experience an attractive force and will flow towards the positive terminal of the battery. Thus, electric current is produced in the collector region.
VCB
VBE

## Slide 12: COMMON-BASE CONFIGURATION
To describe the behavior of common-base amplifiers requires two set of characteristics:
    Input or driving point characteristics.
    Output or collector characteristics
The output voltage VCB (collector-base voltage) is kept constant at zero volts and the input voltage VBE is increased from zero volts to different voltage levels.
Output voltage (VCB) is increased to 10 volts. Input voltage VBE is increased from 0 to different voltage levels.
When output voltage (VCB) is at 0 volts and emitter-base junction is forward biased, the emitter-base junction acts like a normal p-n junction diode. So the input characteristics are same as the forward characteristics of a normal pn junction diode. The cut in voltage of a silicon transistor is 0.7 volts.
When the output voltage (VCB) is increased to 10 volts, the emitter current flow will be increased (reduces the depletion region width at emitter-base junction). As a result, the turn on voltage will be reduced. Therefore, the curves shifted towards the left side for higher values of output voltage VCB.

## Slide 13: COMMON-BASE CONFIGURATION
The output characteristics has 3 basic regions:
    Active region – defined by the biasing arrangements
    Cutoff region – region where the collector current is 0A
    Saturation region- region of the characteristics to the left of VCB = 0V
Active Region: For a constant input current IE, when the output voltage VCB is increased, the output current IC remains constant.
Saturation region:
Both emitter-base junction and collector-base junction are forward biased.
A small increase in the collector voltage VCB there will be higher IC. Same as PN junction.
Cutoff region:
Both are Reverse biased and so flow of current.

## Slide 14: COMMON-BASE CONFIGURATION
VCB=0

## Slide 15: COMMON-BASE CONFIGURATION
ACTIVE REGION | SATURATION REGION | CUTOFF REGION
IE increased, IC increased |  | 
BE junction reverse biased and CB junction reverse biased | BE and CB junctions are forward biased | BE and CB junction are reverse biased
IC ≈ IE |  | No current flow at collector, only leakage current
IC does not depend on VCB | Small change in VCB will cause big difference in IC | 
Suitable region for the transistor to work as an amplifier | The allocation for this region is to the left of the VCB = 0 V | Region below the line of IE = 0

## Slide 16: COMMON-BASE CONFIGURATION
The curves (output characteristics) clearly indicate that a first approximation to the relationship between IE and IC in the active region is given by
IC ≈ IE
Once a transistor is in the ‘on’ state, the base-emitter voltage will be assumed to be
VBE = 0.7V
In the dc mode the level of IC and IE due to the majority carriers are related by a quantity called alpha

## Slide 17: COMMON-BASE CONFIGURATION
It can then be summarized to (ignore ICBO due to small value)
For ac situations where the point of operation moves on the characteristics curve, an ac alpha defined by
Alpha a common base current gain factor that shows the efficiency by calculating the current percent from current flow from emitter to collector. The value of is typical from 0.9 ~ 0.998.

## Slide 18
Thank You