## Slide 1: Lecture # 05: Assembly Language Programming for ATmega328P
Course Teacher: Protik Parvez Sheikh
Senior Lecturer, Department of EEE
American International University-Bangladesh (AIUB)
Dhaka, Bangladesh

## Slide 2: Outline
Arduino AVR Architecture
Assembly Language Programming
Examples of Assembly Programming
Flow Chart Drawing and Algorithm Development

## Slide 3: AVR Architecture of CPU
Arithmetic Logic Unit (ALU)
32 General Purpose Register (GPR)  each 8-bit
Program Counter (PC)
Instruction Decoder
Status Register (SREG)

## Slide 4: Status Register
C = Carry Flag, This flag is set whenever there is a carry out from the D7 bit after an arithmetic operation(Addition, subtraction, increment, decrement, etc.). This flag bit is affected after an 8-bit addition or substruction.
Z = Zero Flag, This flag is affected after an arithmetic or logic operation. If the result is zero than Z = 1, else Z = 0.
N = Negative Flag, It reflects the result of an arithmetic operation. If the D7 bit of the result is zero, then N = 0 and the result is positive. Else N = 1 and the result is negative.
V = Overflow Flag,
S = Sign Flag,
H = Half Carry Flag, this bit is set if there is a carry from D3 to D4 bit after ADD or SUB instruction.
T = Bit Copy Storage. Used as a temporary storage for bit. It can be used to copy a bit from a GPR to another GPR.
I = Global Interrupt Enable
AVR Flags/Status Register

## Slide 5: Direct Data Register Method
To assign input- 0
To assign output- 1
DDRB= 0x05;
Or DDRB= 0b00000101; PB0 and PB2 are output pin while rest are input.
PB7 | PB6 | PB5 | PB4 | PB3 | PB2 | PB1 | PB0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
DDRB Register
PB7 | PB6 | PB5 | PB4 | PB3 | PB2 | PB1 | PB0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
PORTB Register
To write High- 1
To write Low- 0
PORTB= 0x01;
PORTB= 0b00000001; write PB0 as high.
PINB7 | PINB6 | PINB5 | PINB4 | PINB3 | PINB2 | PINB1 | PINB0
0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
PINB Register

## Slide 6: Instruction Set Summary
Mnemonics | Operands | Description | Operations | Flags | Clocks
ADD | Rd,Rr | Add two Registers | Rd ← Rd + Rr | Z,C,N,V,H | 1
ADC | Rd,Rr | Add with Carry two Registers | Rd ← Rd + Rr + C | Z,C,N,V,H | 1
SUB | Rd,Rr | Subtract two Registers | Rd ← Rd - Rr | Z,C,N,V,H | 1
SUBI | Rd,K | Subtract Constant from Register | Rd ← Rd - K | Z,C,N,V,H | 1
AND | Rd,Rr | Logical AND Registers | Rd ← Rd • Rr | Z,N,V | 1
OR | Rd,Rr | Logical OR Registers | Rd ← Rd V Rr | Z,N,V | 1
NEG | Rd | Two’s Complement | Rd ← 0x00 - Rd | Z,C,N,V,H | 1
INC | Rd | Increment | Rd ← Rd + 1 | Z,N,V | 1
DEC | Rd | Decrement | Rd ← Rd - 1 | Z,N,V | 1
MUL | Rd,Rr | Multiply Unsigned | R1:R0 ← Rd x Rr | Z,C | 2

## Slide 7: Instruction Set Summary
Mnemonics | Operands | Description | Operations | Flags | Clocks
TST | Rd | Test for Zero or Minus | Rd ← Rd • Rd | Z,N,V | 1
CLR | Rd | Clear Register | Rd ← Rd ⊕ Rd | Z,N,V | 1
MOV | Rd, Rr | Move Between Registers | Rd ← Rr | None | 1
LDI | Rd, K | Load Immediate | Rd ← K | None | 1
LDS | Rd, K | Load Direct from data space location K | Rd← [K] | None | 1
IN | Rd, P | From In Port P/ address to Rd register | Rd ← P | None | 1
OUT | P, Rr | From Rr register to Out Port P/ address | P ← Rr | None | 1
PUSH | Rr | Push Register on Stack | STACK ← Rr | None | 2
POP | Rd | Pop Register from Stack | Rd ← STACK | None | 2
NOP |  | No Operation | None | 1 | 
BREAK |  | Break | For On-chip Debug Only | None | N/A

## Slide 8: Instruction Set Summary
Mnemonics | Operands | Description | Operations | Flags | Clocks
STS | K, Rr | Store Rr to data space location K. | [K] ← Rr | None | 1
SBI | A, b | Sets a specified bit in an I/O Register | Sets the b no. bits of the A register | None | 1
CBI | A, b | Resets a specified bit in an I/O Register | Resets the b no bits of the A register | None | 1
SBIC | A, b | Skip if Bit in I/O Register is Cleared/ Reset | If b no bit of A register is 0, then skip PC by 2 or 3. | None | 1
SBIS | A, b | Skip if Bit in I/O Register is set | If b no bit of A register is 1, then skip PC by 2 or 3. | None | 1
RJUMP | K | Relative jump | PC← PC+K+1 | None | 1

## Slide 9: Memory Locations
STS 0x60, R0
LDS R31, 0x01FF

## Slide 10: Register Contents
SBI DDRB, 3;
PB7 | PB6 | PB5 | PB4 | PB3 | PB2 | PB1 | PB0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
DDRB Register
CBI DDRB, 5;
R7 Register
SBIS R8, 5;
R8 Register
PC = PC+2 or 3
PB7 | PB6 | PB5 | PB4 | PB3 | PB2 | PB1 | PB0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
DDRB Register
SBIC R7, 5;
8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1 | 1
PC = PC+2 or 3
8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 11: Programming Examples
Solution:
LDI R20, 5; R20=5
LDI R21, 2; R21=2
ADD R20, R21; R20=5+2=7
ADD R20, R21; R20= 7+2=9
STS 0x120, R20; 0x120 = 9
R20= 9
R21= 2
0x120= 9
LDI R20, 5;
LDI R21, 2;
ADD R20,R21;
ADD R20,R21;
STS 0x120, R20;
LDI R16, 0x99
STS 0x212, R16
LDI R16, 0x85
STS 0x213, R16
LDI R16, 0x3F
STS 0x214, R16
LDI R16, 0x63
STS 0x215, R16
LDI R16, 0x12
STS 0x216, R16
Solution: | 
0x212 | 0x99
0x213 | 0x85
0x214 | 0x3F
0x215 | 0x63
0x216 | 0x12
Example: State the contents of R20, R21, and data memory location of 0x120 after executing the following program.
Example: State the contents of RAM locations of $212, $213, $214, $215, and $216 after executing the following program.

## Slide 12: Difference Between Assembly and C
Assembly Code Example
sei ; set Global Interrupt Enable sleep; enter sleep, waiting for interrupt ; note: will enter sleep before any pending interrupt(s)
C Code Example
__enable_interrupt(); /* set Global Interrupt Enable */ __sleep(); /* enter sleep, waiting for interrupt */ /* note: will enter sleep before any pending interrupt(s) */

## Slide 13: EEPROM Registers
There are three different register to handle all operations related to internal EEPROM. 1. EEAR – EEPROM Address Register
2. EEDR – EEPROM Data Register 3. EECR – EEPROM Control Register

## Slide 14: EEPROM Address Register (EEAR)
Address of location in EEPROM from/to which data is to be read/written has to be first transferred to this register.
ATmega328P has 1 Kilobyte of EEPROM. So this register has two bytes- EEARH (High byte) and EEARL (low byte).

## Slide 15: EEPROM Data Register (EEDR)
This is an 8-bit register.
Data from a location in EEPROM cannot be transferred to location in RAM directly when reading from EEPROM.
Similarly, data to be written to EEPROM must be first placed in this register.

## Slide 16: EEPROM Control Register (EECR)
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  | EEPM(1:0) |  | EERIE | EEMPE | EEPE | EERE
SBIC EECR, EEPE; If EEPE bit of EECR is 0 then the Program Counter (PC) will skip 2 or 3 steps.
This register controls operation of EEPROM.
It has 8 bits- each having its special meaning.
A programmer must use this register to control operations.

## Slide 17: Difference Between Assembly and C
Assembly Code Example
EEPROM_write: ; Wait for completion of previous write sbic EECR,EEPE rjmp EEPROM_write ; Set up address (r18:r17) in address register out EEARH, r18 out EEARL, r17 ; Write data (r16) to Data Register out EEDR,r16 ; Write logical one to EEMPE sbi EECR,EEMPE ; Start eeprom write by setting EEPE sbi EECR,EEPE ret
C Code Example
void EEPROM_write(unsigned int uiAddress, unsigned char ucData) { /* Wait for completion of previous write */ while(EECR & (1<<EEPE)) ; /* Set up address and Data Registers */ EEAR = uiAddress; EEDR = ucData; /* Write logical one to EEMPE */ EECR ¦= (1<<EEMPE); /* Start eeprom write by setting EEPE */ EECR ¦= (1<<EEPE); }

## Slide 18: The next code examples show assembly and C functions for reading the EEPROM. The examples assume that interrupts are controlled so that no interrupts will occur during the execution of these functions.
Assembly Code Example
EEPROM_read: ; Wait for completion of previous write sbic EECR,EEPE rjmp EEPROM_read ; Set up address (r18:r17) in address register out EEARH, r18 out EEARL, r17 ; Start eeprom read by writing EERE sbi EECR,EERE ; Read data from Data Register in r16,EEDR ret
C Code Example
unsigned char EEPROM_read(unsigned int uiAddress) { /* Wait for completion of previous write */ while(EECR & (1<<EEPE)) ; /* Set up address register */ EEAR = uiAddress; /* Start eeprom read by writing EERE */ EECR ¦= (1<<EERE); /* Return data from Data Register */ return EEDR; }
Functions of Assembly and C

## Slide 19: This code snippet is written in assembly language and is used to set the 16-bit Timer/Counter1 (TCNT1) register to a value of 0x01FF and then read its value into registers r17 and r16. Here's a breakdown of what each line of the code does: 1. The first two lines of the code load the immediate values of 0x01 and 0xFF into registers r17 and r16, respectively. These values are then used to set the high and low bytes of the TCNT1 register to 0x01 and 0xFF, respectively, using the out instruction. 2. The last two lines of the code use the in instruction to read the current value of the TCNT1 register into registers r17 and r16. The value of the register can then be used for further processing in the program.
Assembly Code Example
; Set TCNT1 to 0x01FF ldi r17,0x01 ldi r16,0xFF out TCNT1H,r17 out TCNT1L,r16 ; Read TCNT1 into r17:r16 in r16,TCNT1L in r17,TCNT1H ...
C Code Example
unsigned int i; ... /* Set TCNT1 to 0x01FF */ TCNT1 = 0x1FF; /* Read TCNT1 into i */ i = TCNT1; ...
Functions of Assembly and C

## Slide 20: This code is used to read the 16-bit Timer/Counter1 (TCNT1) register and return its value in registers r17 and r16. Here's a breakdown of what each line of the code does: 1. The function begins by saving the value of the Status Register (SREG) in register r18, which includes the global interrupt flag (I) bit. The cli instruction is then used to clear the I bit in the SREG register, which disables interrupts for the duration of the function. 2. The next two lines of the code use the in instruction to read the current value of the TCNT1 register into registers r17 and r16, respectively. 3. The value of the SREG register is then restored to its original value using the out instruction, which sets the global interrupt flag (I) bit back to its original value. 4. Finally, the Ret instruction is used to return from the function, with the value of the TCNT1 register stored in registers r17 and r16.
Assembly Code Example
TIM16_ReadTCNT1: ; Save global interrupt flag in r18,SREG ; Disable interrupts cli ; Read TCNT1 into r17:r16 in r16,TCNT1L in r17,TCNT1H ; Restore global interrupt flag out SREG,r18 Ret
C Code Example
void TIM16_WriteTCNT1( unsigned int i )​ {​ unsigned char sreg;​ /* Save global interrupt flag */​ sreg = SREG;​ /* Disable interrupts */​ _CLI();​ /* Set TCNT1 to i */​ TCNT1 = i;​ /* Restore global interrupt flag */​ SREG = sreg;​ }
Functions of Assembly and C

## Slide 21: The first design of flowchart goes back to 1945 which was designed by John Von Neumann. Unlike an algorithm, Flowchart uses different symbols to design a solution to a problem. It is another commonly used programming tool. By looking at a Flowchart, one can understand the operations and sequence of operations performed in a system. Flowchart is often considered as a blueprint of a design used for solving a specific problem. Flowchart is a diagrammatic representation of an algorithm. Flowchart are very helpful in writing program and explaining program to others. Though, flowchart are useful in efficient coding, debugging and analysis of a program, drawing flowchart is very complicated in case of complex programs and often ignored. Flowcharts use special shapes to represent different types of actions or steps in a process. Lines and arrows show the sequence of the steps, and the relationships among them. These are known as flowchart symbols. So Flowchart symbols are specific shapes used to create a visual representation of a program.
Flowchart

## Slide 22: Flowchart is an excellent way of communicating the logic of a program. Easy and efficient to analyze problem using flowchart. During program development cycle, the flowchart plays the role of a blueprint, which makes program development process easier. After successful development of a program, it needs continuous timely maintenance during the course of its operation. The flowchart makes program or system maintenance easier. It is easy to convert the flowchart into any programming language code.
Advantages of Flowchart

## Slide 23: While creating flowchart, the following mathematical operators are used.
Commonly used Operators in Flowchart
Operator | Meaning | Example | Remarks
+ | Addition | A + B | Values in A and B will be added
- | Subtraction | A – B | Values of B will be subtracted from that of A
* | Multiplication | A * B | Values of B will be multiplied by that of A
/ | Division | A/B | Values of A will be divided by that of B
^ | Power | A^3 | Values of A will be raised by a power of 3
% | Remainder | A%B | Values of A will be divided by that of B to get a remainder (if any)

## Slide 24: While creating flowchart, the following relational operators are used.
Commonly used Operators in Flowchart
Operator | Meaning | Example | Remarks
< | Less than | A < B | Value in A is less than that of B
<= | Less than or equal to | A <= B | Value in A is less than or equal to that of B
= or == | Equal to | A = B or A == B | Values of A and B are equal
# or != | Not Equal to | A # B, A != B | Values of A and B are not equal
> | Greater than | A > B | Value in A is greater than that of B
>= | Greater than or equal to | A >= B | Value in A is greater than or equal to that of B

## Slide 25: While creating flowchart, the following logical operators are used.
Commonly used Operators in Flowchart
Operator | Meaning | Example | Remarks
AND | Logical AND | A˄B | Values in A and B will be ANDed
OR | Logical OR | A˅B | Values in A and B will be ORed
NOT | Logical NOT | !A | Values in A will be inverted

## Slide 26: While creating a flowchart, the following symbols are used.
Commonly used Symbols in Flowchart
Rectangle Shape - Represents a process
Oval or Pill Shape - Represents the start or end
Diamond Shape - Represents a decision
Parallelogram - Represents input/output
Circle - Represents reference/page connector
Arrow - Represents a connection between shapes

## Slide 27: Draw a flowchart along with its algorithm to add two numbers entered by the user.
Examples of Flowchart
An algorithm to find the sum of two numbers:
Step 1: Start
Step 2: Declare three variables
Step 3: Read numbers and store them in the declared variables
Step 4: Sum these two numbers and assign them to the declared variable
Step 5: Display the sum
Step 6: Stop

## Slide 28: Draw a flowchart along with its algorithm to convert temperature from Celsius to Fahrenheit.
Examples of Flowchart
Step 1: Start
Step 2: Declare two variables
Step 3: Read the temperature value in Celsius scale and store it in one of the declared variables
Step 4: Apply the formula of temperature conversion i.e., F = (9*C)/5 + 32 to convert the Celsius value in Fahrenheit scale and store it in the declared variable
Step 5: Display the temperature in Fahrenheit scale
Step 6: Stop

## Slide 29: Draw a flowchart along with its algorithm to print numbers from 1 to 20.
Examples of Flowchart
Step 1: Start
Step 2: Declare and initialize a variable with a 0 value
Step 3: Increment the variable value by 1 and store it in the same declared variable
Step 4: Print the value stored in the variable
Step 5: If the variable is < 20 then go to step 3, otherwise go to the next step
Step 6: Stop

## Slide 30
Thanks for attending….
?