## Slide 1
Electronic Devices
Faculty Name: Dr. Mohammad Alif Arman
Email : dr.alifarman@aiub.edu
Reference book:
Electronic Devices and Circuit Theory (Chapter-1)
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Mid Term Lecture - 01

## Slide 2
Introduction
The technology advancing so fast and so the fundamental principles. Systems are incredibly smaller, current speeds of operation are truly remarkable, and new gadgets surface every day, leaving us to wonder where technology is taking us.

## Slide 3
Complete systems now appear on wafers thousands of times smaller than the single element of earlier networks.
Figure 1.1: Jack St. Clair Kilby, inventor (1958) of the integrated circuit and co-inventor of the electronic handheld calculator. (Texas Instruments.)
Introduction Contd.

## Slide 4
Today, the Intel® CoreTM i7 Extreme Edition Processor of Fig. 1.2 has 731 million transistors in a package that is only slightly larger than a 1.67 sq. inches.
In 1965, Dr. Gordon E. Moore presented a paper predicting that the transistor count in a single IC chip would double every two years.
Now, more than 45 years, later we find that his prediction is amazingly accurate and expected to continue for the next few decades.
Figure 1.2: Intel® Core™ i7 Extreme Edition Processor.
Introduction Contd.

## Slide 5
Materials

## Slide 6
Why do we use semiconductors instead of conductors in electronics fabrication?
To control.
Transistors need to be able to give us two different outputs to perform logic functions; that is "1" (on) and "0" (off). In short switching ability.

## Slide 7
Semiconductor materials have a negative temperature coefficient.
Semiconductor materials, however, exhibit an increased level of conductivity with the application of heat. As the temperature rises, an increasing number of valence electrons absorb sufficient thermal energy to break the covalent bond and to contribute to the number of free carriers.
For conductors, the resistance increases with an increase in heat. This is because the numbers of carriers in a conductor do not increase significantly with temperature, but their vibration pattern about a relatively fixed location makes it increasingly difficult for a sustained flow of carriers through the material.
Materials that react in this manner are said to have a positive temperature coefficient.
Why do we use semiconductors instead of conductors in electronics fabrication?

## Slide 8
The construction of every discrete (individual) solid-state (hard crystal structure) electronic device or integrated circuit begins with a semiconductor material (of the highest quality).
Semiconductors are elements having a conductivity between that of a good conductor and that of an insulator.
In general, semiconductor materials fall into one of two classes: single-crystal and compound.
Single-crystal semiconductors such as germanium (Ge) and silicon (Si) have a repetitive crystal structure, whereas compound semiconductors such as gallium arsenide (GaAs), cadmium sulfide (CdS), gallium nitride (GaN), and gallium arsenide phosphide (GaAsP) are constructed of two or more semiconductor materials of different atomic structures.
Ge, Si, and GaAs semiconductors used most frequently in the construction of electronic devices.
Semiconductor Materials: Ge, SI & GaAs
What is single-crystal and compound?

## Slide 9
Germanium:
In the first few decades following the discovery of the diode in 1939 and the transistor in 1947 germanium was used almost exclusively because it was relatively easy to find and was available in fairly large quantities.
It was also relatively easy to refine to obtain very high levels of purity, an important aspect in the fabrication process.
However, it was discovered in the early years that diodes and transistors constructed using germanium as the base material suffered from low levels of reliability due primarily to its sensitivity to changes in temperature.
Semiconductor Materials: Ge, SI & GaAs Contd.

## Slide 10
Silicon:
At the time, scientists were aware that another material, silicon, had improved temperature sensitivities, but the refining process for manufacturing silicon of very high levels of purity was still in the development stages. In 1954 the first silicon transistor was introduced, and silicon quickly became the semiconductor material of choice due to,
Silicon is Less temperature sensitive
one of the most abundant materials on earth, removing any concerns about availability.
Semiconductor Materials: Ge, SI & GaAs Contd.

## Slide 11
Gallium Arsenide:
As time moved on, however, the field of electronics became increasingly sensitive to issues of speed.
Scientist developed the first compound material GaAs transistor in the early 1970s.
The speed of operation: up to FIVE times that of Si.
GaAs was more difficult to manufacture at high levels of purity, was more expensive, and had little design support in the early years of development.
However, in time the demand for increased speed resulted in more funding for GaAs research, to the point that today it is often used as the base material for new high-speed, very large scale integrated (VLSI) circuit designs.
Semiconductor Materials: Ge, SI & GaAs Contd.

## Slide 12
To fully appreciate why Si, Ge, and GaAs are the semiconductors of choice for the electronics industry requires some understanding of the atomic structure of each and how the atoms are bound together to form a crystalline structure.
The fundamental components of an atom are the electron, proton, and neutron.
In the lattice structure, neutrons and protons form the nucleus and electrons appear in fixed orbits around the nucleus. The Bohr model for the three materials is provided in Fig. 1.3.
Covalent Bonding and Intrinsic Materials

## Slide 13
As indicated in Fig. 1.3, silicon has 14 orbiting electrons, germanium has 32 electrons, gallium has 31 electrons, and arsenic has 33 orbiting electrons (the same arsenic that is a very poisonous chemical agent).
For germanium and silicon there are four electrons in the outermost shell, which are referred to as valence electrons.
Gallium has three valence electrons and arsenic has five valence electrons.
Atoms that have four valence electrons are called tetravalent, those with three are called trivalent, and those with five are called pentavalent.
The term valence is used to indicate that the potential (ionization potential) required to remove any one of these electrons from the atomic structure is significantly lower than that required for any other electron in the structure.
Covalent Bonding & Intrinsic Materials Contd.

## Slide 14
In a pure silicon or germanium crystal the four valence electrons of one atom form a bonding arrangement with four adjoining atoms, as shown in Fig. 1.4.
This bonding by the sharing of electrons, is called covalent bonding.
Covalent Bonding & Intrinsic Materials Contd.

## Slide 15
Because GaAs is a compound semiconductor, there is sharing between the two different atoms, as shown in Fig. 1.5.
Each atom, gallium or arsenic, is surrounded by atoms of the complementary type. Here five electrons are provided by the As atom and three by the Ga atom.
Covalent Bonding & Intrinsic Materials Contd.

## Slide 16
Gallium Arsenide:
Semiconductor Materials: Ge, SI & GaAs Contd.
c

## Slide 17
Although the covalent bond will result in a stronger bond between the valence electrons and their parent atom, it is still possible for the valence electrons to absorb sufficient kinetic energy from external natural causes to break the covalent bond and assume the “free” state.
The term free is applied to any electron that has separated from the fixed lattice structure and is very sensitive to any applied electric fields such as established by voltage sources or any difference in potential.
The external causes include effects such as light energy in the form of photons and thermal energy (heat) from the surrounding medium.
At room temperature there are approximately 1.5 * 1010 free carriers in 1 cm3 of intrinsic silicon material, that is, 15,000,000,000 (15 billion) electrons in a space smaller than a small sugar cube - an enormous number.
Covalent Bonding & Intrinsic Materials Contd.
What is FREE Electron?

## Slide 18
The term intrinsic is applied to any semiconductor material that has been carefully refined to reduce the number of impurities to a very low level-essentially as pure as can be made available through modern technology.
The free electrons in a material due only to external causes are referred to as intrinsic carriers. Table1.1 compares the number of intrinsic carriers per cubic centimeter(abbreviated ni) for Ge, Si, and GaAs.
Covalent Bonding & Intrinsic Materials Contd.

## Slide 19
It is interesting to note that Ge has the highest number of free electron and GaAs the lowest.
In fact, Ge has more than twice the number as GaAs.
The number of carriers in the intrinsic form is important, but other characteristics of the material are more significant in determining its use in the field.
One such factor is the relative mobility (µn) of the free carriers in the material, that is, the ability of the free carriers to move throughout the material.
Table 1.2 clearly reveals that the free carriers in GaAs have more than five times the mobility of free carriers in Si, a factor that results in response times using GaAs electronic devices that can be up to five times those of the same devices made from Si.
Note also that free carriers in Ge have more than twice the mobility of electrons in Si, a factor that results in the continued use of Ge in high-speed radio frequency applications.
Covalent Bonding & Intrinsic Materials Contd.

## Slide 20
Extremely high levels of purity are necessary because the addition of one part of impurity (of the proper type) per million in a wafer of silicon material can change that material from a relatively poor conductor to a good conductor of electricity.
The ability to change the characteristics of a material through this process is called doping, something that germanium, silicon, and gallium arsenide readily and easily accept.
One important and interesting difference between semiconductors and conductors is their reaction to the application of heat.
Covalent Bonding & Intrinsic Materials Contd.

## Slide 21
Within the atomic structure of each and every isolated atom there are specific energy levels associated with each shell and orbiting electron, as shown in Fig. 1.6.
The energy levels associated with each shell will be different for every element.
The farther an electron is from the nucleus, the higher is the energy state, and any electron that has left its parent atom has a higher energy state than any electron in the atomic structure.
Energy Levels

## Slide 22
Energy Levels Contd.

## Slide 23
The characteristics of a semiconductor material can be altered significantly by the addition of specific impurity atoms to the relatively pure semiconductor material.
These impurities, although only added at 1 part in 10 million, can alter the band structure sufficiently to totally change the electrical properties of the material.
A semiconductor material that has been subjected to the doping process is called an extrinsic material.
There are two extrinsic materials of massive importance to semiconductor device fabrication: n -type and p -type materials.
n-Type & p-Type Materials

## Slide 24
An n -type material is created by introducing impurity elements that have five valence electrons (pentavalent), such as antimony, arsenic, and phosphorus. (Group V elements in Periodic Table)
The effect of such impurity elements is indicated in Fig. 1.7 (using antimony as the impurity in a silicon base).
n-Type Material

## Slide 25
Note that the four covalent bonds are still present. There is, however, an additional fifth electron due to the impurity atom, which is unassociated with any particular covalent bond.
This remaining electron, loosely bound to its parent (antimony) atom, is relatively free to move within the newly formed n -type material.
Diffused impurities with five valence electrons are called donor atoms.
It is important to realize that even though a large number of free carriers have been established in the n -type material, it is still electrically Positive or negative?
neutral since ideally the number of positively charged protons in the nuclei is still equal to the number of free and orbiting negatively charged electrons in the structure.
n-Type Material Contd.

## Slide 26
Those free electrons due to the added impurity sit at this energy level and have less difficulty absorbing a sufficient measure of thermal energy to move into the conduction band at room temperature.
n-Type Material Contd.
Conductivity of the material will increase or decrease?
The result is that at room temperature, there are a large number of carriers (electrons) in the conduction level, and the conductivity of the material increases significantly.
In which application this process is crucial?
Photo electric effect – Solar cell

## Slide 27
The p -type material is formed by doping a pure germanium or silicon crystal with impurity atoms having three valence electrons.
The elements most frequently used for this purpose are boron, gallium, and indium. (Group III elements in Periodic Table)
Note that there is now an insufficient number of electrons to complete the covalent bonds of the newly formed lattice.
p-Type Material

## Slide 28
The resulting vacancy is called a hole and is represented by a small circle or a plus sign, indicating the absence of a negative charge.
Since the resulting vacancy will readily accept a free electron:
The added impurities with three valence electrons are called acceptor atoms.
The resulting p -type material is electrically - +?
neutral, for the same reasons described for the n -type material.
p-Type Material Contd.

## Slide 29
The effect of the hole on conduction is shown in Fig. If a valence electron acquires sufficient kinetic energy to break its covalent bond and fills the void created by a hole, then a vacancy, or hole, will be created in the covalent bond that released the electron.
Electron vs Hole Flow

## Slide 30
In an n-type material ( Fig. a ) the electron is called the majority carrier and the hole the minority carrier.
In a p-type material the hole is the majority carrier and the electron is the minority carrier.
Majority & Minority Carriers

## Slide 31
Knowledge
  Basic of semiconductor
  Doping principles
  Crystal Structure
Importance and principles of Semiconductor
  Control electronics
  Semiconductor materials have a negative temperature coefficient.
Practical applications
  Logic Circuit
  CPU
  Diode
  Solar cell
Outcome

## Slide 32
Electronic Devices
Reference book:
Electronic Devices and Circuit Theory (Chapter-1)
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Mid Term Lecture - 02
Faculty Name: Dr. Mohammad Alif Arman
Email : dr.alifarman@aiub.edu
Room: DN0526

## Slide 33
Develop a clear understanding of the basic operation and characteristics of a diode in the no-bias, forward-bias, and reverse-bias regions.
Be able to calculate the dc, ac, and average ac resistance of a diode from the characteristics.
Understand the impact of an equivalent circuit whether it is ideal or practical.
Become familiar with the operation and characteristics of a Zener diode and light- emitting diode.
Objectives

## Slide 34
Now that both n – and p -type materials are available, we can construct our first solid-state electronic device: The semiconductor diode, with applications too numerous to mention, is created by simply joining an n -type and a p -type material together.
In the absence of an applied bias across a semiconductor diode, the net flow of charge in one direction is zero.
Semiconductor Diode: No Applied Bias (V=0 V)

## Slide 35
No Applied Bias (VD=0 V)

## Slide 36
The current that exists under reverse-bias conditions is called the reverse saturation current and is represented by Is .
Reverse-Bias Condition (VD<0 V)

## Slide 37
Forward-Bias Condition (VD>0 V)
A forward-bias or “on” condition is established by applying the positive potential to the p -type material and the negative potential to the n -type material as shown in Fig. 1.14 .

## Slide 38
It can be demonstrated through the use of solid-state physics that the general characteristics of a semiconductor diode can be defined by the following equation, referred to as Shockley’s equation, for the forward- and reverse-bias regions:
Where, Is is the reverse saturation current
VD is the applied forward-bias voltage across the diode
n is an ideality factor, which is a function of the operating conditions and physical construction; it has a range between 1 and 2 depending on a wide variety of factors (n = 1 will be assumed throughout this text unless otherwise noted).
Forward-Bias Condition (VD>0 V) Contd.

## Slide 39
The voltage VT in Eq. (1.1) is called the thermal voltage and is determined by:
where k is Boltzmann’s constant = 1.38 * 10-23 J/K
TK is the absolute temperature in kelvins = 273 + the temperature in °C
q is the magnitude of electronic charge = 1.6 * 10-19 C
Forward-Bias Condition (VD>0 V) Contd.

## Slide 40
Semiconductor Diode Characteristics

## Slide 41
The maximum reverse-bias potential that can be applied before entering the breakdown region is called the peak inverse voltage (referred to simply as the PIV rating) or the peak reverse voltage (denoted the PRV rating).
If an application requires a PIV rating greater than that of a single unit, a number of diodes of the same characteristics can be connected in series. Diodes are also connected in parallel to increase the current-carrying capacity.
In general, the breakdown voltage of GaAs diodes is about 10% higher those for silicon diodes but after 200% higher than levels for Ge diodes.
Breakdown Region

## Slide 42
As the voltage across the diode increases in the reverse-bias region, the velocity of the minority carriers responsible for the reverse saturation current Is?
Eventually, their velocity and associated kinetic energy (WK = 1/2 mv2) will be sufficient to release additional carriers through collisions with otherwise stable atomic structures.
An ionization process will result whereby valence electrons absorb sufficient energy to leave the parent atom.
These additional carriers can then aid the ionization process to the point where a high avalanche current is established and the avalanche breakdown region determined.
Breakdown Region Contd.
will also increase.

## Slide 43
The avalanche region (VBV) can be brought closer to the vertical axis by increasing the doping levels in the p- and n-type materials.
However, as VBV decreases to very low levels, such as -5 V, another mechanism, called Zener breakdown, will contribute to the sharp change in the characteristic.
It occurs because there is a strong electric field in the region of the junction that can disrupt the bonding forces within the atom and “generate” carriers.
Although the Zener breakdown mechanism is a significant contributor only at lower levels of VBV, this sharp change in the characteristic at any level is called the Zener region, and diodes employing this unique portion of the characteristic of a p–n junction are called Zener diodes.
Breakdown Region Contd.

## Slide 44
Ge, Si & GaAs
Knee voltage is the forward voltage at which the flow of the current through the PN junction of the diode increases rapidly.

## Slide 45
In the forward-bias region the characteristics of a silicon diode shift to the left at a rate of 2.5 mV per centigrade degree increase in temperature.
In the reverse-bias region the reverse current of a silicon diode doubles for every 10°C rise in temperature.
The reverse breakdown voltage of a semiconductor diode will increase or decrease with temperature.
As temperature increases it adds energy to the diode:
    It reduces the required forward bias voltage for forward bias conduction.
    It increases the amount of reverse current in the reverse bias condition.
    It increases maximum reverse bias avalanche voltage.
Germanium diodes are more sensitive to temperature variations than silicon or gallium arsenide diodes.
Temperature Effects

## Slide 46
Temperature Effect Contd.
In the reverse-bias region the reverse current of a silicon diode doubles for every 10°C rise in temperature.
In the forward-bias region the characteristics of a silicon diode shift to the left at a rate of 2.5 mV per centigrade degree increase in temperature.
Finally, The reverse breakdown voltage of a semiconductor diode will increase or decrease with temperature.

## Slide 47
The semiconductor diode behaves in a manner similar to a mechanical switch in that it can control whether current will flow between its two terminals.
The semiconductor diode is different from a mechanical switch in the sense that when the switch is closed it will only permit current to flow in one direction.
Ideal vs Practical

## Slide 48
Ideally, if the semiconductor diode is to behave like a closed switch in the forward-bias region, the resistance of the diode should be 0 Ω.
In the reverse-bias region its resistance should be ∞ Ω to represent the open-circuit equivalent.
Ideal vs Practical Contd.

## Slide 49
Semiconductors react differently to DC and AC currents.
There are three types of resistance:
        DC (static) resistance
        AC (dynamic) resistance
        Average AC resistance
Resistance Levels

## Slide 50
For a specific applied DC voltage VD, the diode has a specific current ID, and a specific resistance RD.
In general, therefore, the higher the current through a diode, the lower is the dc resistance level.
DC or Static Resistance
I
R

## Slide 52
The dc resistance of a diode is independent of the shape of the characteristic in the region surrounding the point of interest.
The designation Q-point is derived from the word quiescent, which means “still or unvarying.”
In general, therefore, the lower the Q-point of operation (smaller current or lower voltage), the higher is the ac resistance.
See Example 1.4.
AC or Dynamic Resistance

## Slide 53
In the forward bias region:
The resistance depends on the amount of current (ID) in the diode.
The voltage across the diode is fairly constant (26 mV for 25°C).
rB ranges from a typical 0.1 Ω for high power devices to 2 Ω for low power, general purpose diodes. In some cases rB can be ignored.
In the reverse bias region:
The resistance is effectively infinite. The diode acts like an open.
AC or Dynamic Resistance Contd.

## Slide 54
The average ac resistance is, by definition, the resistance determined by a straight line drawn between the two intersections established by the maximum and minimum values of input voltage.
Average AC or Resistance

## Slide 55
Average AC or Resistance
Vmin = 0.65v Imin = 2mA
Vmax = 0.725v Imax = 17mA
Vd = 0.725 – 0.65 = 0.075V
Id = 17 – 2 = 15mA
Rav = 0.075/15 = 5ohm
Rd Vd = 0.65 > 5 ohm
Rd Vd = 0.725 < 5 ohm

## Slide 56
Summary table

## Slide 57
An equivalent circuit is a combination of elements properly chosen to best represent the actual terminal characteristics of a device or system in a particular operating region.
Diode Equivalent Circuits

## Slide 58
Thank You

## Slide 59
Knowledge
  Basic of PN Junction
  Forward, reverse bias and zero bias voltage
  Resistance
Principles of Semiconductor growth mechanism
Practical applications
  Circuit
  Working principle of Diode
  Diodes can perform switching and digital logic operations.
Outcome

## Slide 60
Electronic Devices
Reference book:
Electronic Devices and Circuit Theory (Chapter-2)
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Mid Term Lecture - 03
Faculty Name: Dr. Mohammad Alif Arman
Email : dr.alifarman@aiub.edu
Room: DN0526

## Slide 61: Objectives
Understand the concept of load-line analysis and how it is applied to diode networks.
Become familiar with the use of equivalent circuits to analyze series, parallel, and series-parallel diode networks.

## Slide 62: LOAD-LINE ANALYSIS
A load line is a line drawn on the IV characteristics curve.
The load line plots all possible combinations of diode current (ID) and voltage (VD) for a given circuit.
The maximum ID equals E/R, and the maximum VD equals E.
The point where the load line and the characteristic curve intersect is the Q-point, which identifies ID and VD for a particular diode in a given circuit.

## Slide 63: LOAD-LINE ANALYSIS

## Slide 64: LOAD-LINE ANALYSIS

## Slide 65: LOAD-LINE ANALYSIS

## Slide 66
SERIES DIODE CONFIGURATIONS

## Slide 67
SERIES DIODE CONFIGURATIONS
Replace with equivalent Circuit

## Slide 68
SERIES DIODE CONFIGURATIONS
Replace with equivalent Circuit

## Slide 69
SERIES DIODE CONFIGURATIONS

## Slide 70: SERIES DIODE CONFIGURATIONS

## Slide 71: SERIES DIODE CONFIGURATIONS

## Slide 72: SERIES DIODE CONFIGURATIONS

## Slide 73: SERIES DIODE CONFIGURATIONS
Applying KVL,

## Slide 74: SERIES-PARALLEL CONFIGURATIONS
See Example 2.11

## Slide 75: SERIES-PARALLEL CONFIGURATIONS

## Slide 76: SERIES-PARALLEL CONFIGURATIONS
See Example 2.14 and 2.15

## Slide 77
Thank You

## Slide 78
Electronic Devices
Reference book:
Electronic Devices and Circuit Theory (Chapter-2)
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Mid Term Lecture - 04
Faculty Name: Dr. Mohammad Alif Arman
Email : dr.alifarman@aiub.edu
Room: DN0526

## Slide 79
Understand the process of rectification to establish a dc level from a sinusoidal ac input.
Objectives

## Slide 80: SINUSOIDAL INPUTS; HALF-WAVE

## Slide 81: HALF-WAVE RECTIFICATION
The process of removing one-half the input signal to establish a dc level is called halfwave rectification.
The effect of using a silicon diode with VK = 0.7 V is demonstrated in below Figure for the forward-bias region. The applied signal must now be at least 0.7 V before the diode can turn “on.”

## Slide 82: HALF-WAVE RECTIFICATION

## Slide 83: HALF-WAVE RECTIFICATION

## Slide 84: PIV (PRV)
It is the voltage rating that must not be exceeded in the reverse-bias region or the diode will enter the Zener avalanche region.
Applying Kirchhoff’s voltage law, it is fairly obvious that the PIV rating of the diode must equal or exceed the peak value of the applied voltage.

## Slide 85: FULL-WAVE RECTIFICATION: BRIDGE NETWORK

## Slide 86: BRIDGE NETWORK

## Slide 87: BRIDGE NETWORK

## Slide 88: CENTER-TAPPED TRANSFORMER
Network conditions for the positive region of vi

## Slide 89: CENTER-TAPPED TRANSFORMER
Network conditions for the negative region of vi

## Slide 91
Thank You

## Slide 92
Electronic Devices
Reference book:
Electronic Devices and Circuit Theory (Chapter-2)
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Mid Term Lecture - 05
Faculty Name: Dr. Mohammad Alif Arman
Email : dr.alifarman@aiub.edu
Room: DN0526

## Slide 93: Objectives
Be able to predict the output response of a clipper and clamper diode configuration.

## Slide 94
Clippers are networks that employ diodes to “clip” away a portion of an input signal without distorting the remaining part of the applied waveform.
The half-wave rectifier is an example of the simplest form of diode clipper- one resistor and a diode. Depending on the orientation of the diode, the positive or negative region of the applied signal is “clipped” off.
There are two general categories of clippers: series and parallel.
The series configuration is defined as one where the diode is in series with the load, whereas the parallel variety has the diode in a branch parallel to the load.
CLIPPERS

## Slide 95: CLIPPERS: SERIES
Diode is in series with the load.

## Slide 96: Series Clipper with a dc supply

## Slide 97: CLIPPERS: SERIES
Use transition voltage to define “on” and “off” regions
Draw the output waveform directly below the applied voltage using the same scales for the horizontal axis and the vertical axis.
Negative half cycle clipped away in output waveform

## Slide 98: CLIPPERS: SERIES
Determine transition level

## Slide 99: CLIPPERS: SERIES
For vi = 20 V (0 --> T/2) the network results,
The diode is in the short-circuit state.
vo = 20V + 5V = 25V

## Slide 100
For vi = -10 V (T/2 --> T) the network results,
The diode is in the “off” state.
vo = iRR = (0)R = 0 V
The resulting output voltage corresponds to input voltage appears as:

## Slide 101: CLIPPERS: PARALLEL
Diode in a branch parallel to the load.

## Slide 102: CLIPPERS: PARALLEL
Determine output across the series combination of the diode and the 4-V supply
Determine transition level of input voltage.
Condition:
Replace circuit with short-circuit equivalent.
Diode current is 0 mA.

## Slide 103
For , diode is on.
For , diode is off.

## Slide 104: CLIPPERS: PARALLEL
Si
Determine transition level of input voltage.
Condition:
Replace circuit with diode equivalent circuit.
Diode current is 0 mA.
Applying KVL around output loop in clockwise direction,

## Slide 105
For , ID direction is counter-clockwise.
Diode is off.
For , ID direction is counter-clockwise
Diode is on.

## Slide 106: CLIPPERS
Simple Series clippers (Ideal Diodes) for the sinusoidal input
Biased Series Clippers (Ideal Diodes)

## Slide 107: CLIPPERS
Simple Parallel clippers (Ideal Diodes) for the sinusoidal input
Biased Parallel Clippers (Ideal Diodes)

## Slide 108: CLAMPERS
A clamper is a network constructed of a diode, a resistor, and a capacitor that shifts a waveform to a different dc level without changing the appearance of the applied signal.
The output signal is clamped to 0 V for the interval 0 to T/2 but maintains the same total swing (2V ) as the input.

## Slide 109
Step 1: Start the analysis by examining the response of the portion of the input signal that will forward bias the diode.
Step 2: During the period that the diode is in the “on” state, assume that the capacitor will charge up instantaneously to a voltage level determined by the surrounding network.
Step 3: Assume that during the period when the diode is in the “off” state the capacitor holds on to its established voltage level.
For the interval 0 -> T/2 :
For the interval T/2 -> T :
CLAMPERS

## Slide 110
Step 4: Throughout the analysis, maintain a continual awareness of the location and defined polarity for vo to ensure that the proper levels are obtained.
Step 5: Check that the total swing of the output matches that of the input.
The output signal maintains the same total swing (2V) as the input.

## Slide 111: CLAMPERS
From t1 to t2 period of the input signal the diode will be forward biased.

## Slide 112
From t2 to t3 period of the input signal the diode will be reverse biased
The output swing of 30 V matches the input swing.
See Example 2.23

## Slide 113: Clamping Networks

## Slide 114
Thank You

## Slide 115
Electronic Devices
Reference book:
Electronic Devices and Circuit Theory (Chapter-2)
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Mid Term Lecture - 06
Faculty Name: Dr. Mohammad Alif Arman
Email : dr.alifarman@aiub.edu
Room: DN0526

## Slide 116: Objectives
Become familiar with the analysis of and the range of applications for Zener diodes.

## Slide 117: ZENER REGION
If the Diode is reverse biased and the voltage is increased, a point will be reached when the diode enters reverse breakdown and current will flow with a very rapid rate.
The direction of this current will be opposite to that of the positive voltage region.
The reverse bias potential that results in this dramatic change in characteristics is called the Zener Potential /Voltage and is given by the symbol Vz.
The reverse or Avalanche breakdown is often termed as Zener Breakdown (at very low levels).
The region where this sharp change in characteristics occur is known as Zener or Avalanche breakdown region and the current is termed as avalanche current.

## Slide 118
The maximum reverse-bias potential that can be applied before entering the Zener Region is called the peak inverse voltage (referred to simply as the PIV rating) or the peak reverse voltage (denoted by PRV rating).
ZENER REGION

## Slide 119
Diodes that employ the dramatic characteristics of a p-n junction are called Zener Diodes.
Therefore, a Zener diode operates in reverse bias.
Common Zener Voltages: 1.8V to 200V.
ZENER DIODE

## Slide 120
The state of the diode must be determined followed by a substitution of the appropriate model and a determination of the unknown quantities of the network.
The off state is defined by a voltage less than Vz but greater than 0V. The Zener equivalent is the open circuit.
ZENER DIODE

## Slide 121
The Zener diode is a heavily doped diode which, as a result of doping, has a very narrow depletion region. This allows the diode to be operated in the reverse biased region of the characteristic curve without damaging the PN junction.
“Zener Effect”: The area of Zener diode operation (<5V) where the Diode maintains a constant voltage output while operating reverse biased.
“Avalanche Effect”: >5V applied to the diode while reverse biased which tends to cause the diode to eventually breakdown due to heat generation within the lattice structure of the crystal.
ZENER DIODE

## Slide 122
Because of its higher temperature and current capability, silicon is usually preferred in manufacture of Zener Diodes.
Zener Diodes provide a stable reference voltage for use in power supplies, voltmeter & other instruments, voltage regulators.
ZENER DIODE

## Slide 123
ZENER DIODE EXAMPLE

## Slide 124
ZENER DIODE EXAMPLE

## Slide 125: 1st CONDITION: Vi AND R FIXED
The simplest of Zener diode regulator networks appears in Fig. 2.112 . The applied dc voltage is fixed, as is the load resistor. The analysis can fundamentally be broken down into two steps.
1. Determine the state of the Zener diode by removing it from the network and calculating the voltage across the resulting open circuit.
If V ≥ VZ, the Zener diode is on, and the appropriate equivalent model can be substituted.
If V < VZ, the diode is off, and the open-circuit equivalence is substituted.

## Slide 126: 1st CONDITION: Vi AND R FIXED
2. Substitute the appropriate equivalent circuit and solve for the desired unknowns.
For the network of Fig. 2.112 , the “on” state will result in the equivalent network of Fig.2.114 . Since voltages across parallel elements must be the same, we find that
The power dissipated by the Zener diode is determined by
That must be less than the PZM specified for the device.

## Slide 127: 1st CONDITION: Vi AND R FIXED

## Slide 128: 1st CONDITION: Vi AND R FIXED

## Slide 129: 1st CONDITION: Vi AND R FIXED

## Slide 130
Due to the offset voltage Vz, there is a specific range of resistor values (and therefore load current) which will ensure that the Zener diode is in the on state.
Too small RL  VL < Vz  Zener diode will be in the off state.
To determine the min RL that will turn the Zener diode on :
Any load resistance value greater than the RL min will ensure that the Zener diode is in the on state and the diode can be replaced by its Vz source equivalent.
The max IL
2nd CONDITION: FIXED Vi, VARIABLE RL

## Slide 131
Once the diode is in the on state, the voltage across R remains fixed at:
Iz is limited to IZM as provided on the data sheet, it does affect the range of RL and therefore IL.
The maximum load resistance
See Example 2.27.
2nd CONDITION: FIXED Vi, VARIABLE RL

## Slide 132
For fixed values of RL, the voltage Vi must be sufficiently large to turn the Zener diode on. The min turn-on voltage Vi=Vi min :
The max value of Vi is limited by the max Zener current IZM.
Since IL is fixed at VZ/RL and IZM is the max value of IZ, the max Vi is defined by:
3rd CONDITION: FIXED RL, VARIABLE Vi

## Slide 133
3rd CONDITION: FIXED RL, VARIABLE Vi

## Slide 134
Thank You

## Slide 135
Electronic Devices
Reference book:
Electronic Devices and Circuit Theory (Chapter-3)
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Mid Term Lecture - 07
Faculty Name: Dr. Mohammad Alif Arman
Email : dr.alifarman@aiub.edu
Room: DN0526

## Slide 136
P
N
P
Collector
Emitter
Base
The term bipolar indicates that, both electrons and holes contributes to the flow of current.
Three doped regions. The Emitter, the Base and the Collector.
Based on the doping of these three regions, it is known as either NPN or PNP transistor.
There are two PN junctions.

## Slide 137
P
N
P
Collector
Emitter
Base
HOLES
ELECTORNS

## Slide 138
P
N
P
Collector
Emitter
Base
Emitter Heavily Doped
Base Lightly Doped and Very Thin
Collector Moderately Doped
In case of the NPN transistor, the current will flow from the Base towards the Emitter.
PNP transistor, then the current will flow from the Emitter towards the Base region.
B
E
C
N
P
N
P
N
P
B
E
C

## Slide 139: TRANSISTOR OPERATION
The basic operation will be described using the p-n-p transistor.
The operation of the n-p-n transistor is exactly the same if the roles played by the electron and hole are interchanged.
One p-n junction of a transistor is reverse-biased, whereas the other is forward-biased.

## Slide 140: TRANSISTOR OPERATION
Both biasing potentials have been applied to a p-n-p transistor and resulting majority and minority carrier flows indicated.
Majority carriers (+) will diffuse across the forward-biased p-n junction into the n-type material.
A very small number of carriers (+) will go through n-type material to the base terminal. Resulting IB is typically in order of microamperes.
The large number of majority carriers will diffuse across the reverse-biased junction into the p-type material connected to the collector terminal.

## Slide 141: TRANSISTOR OPERATION
Majority carriers can cross the reverse-biased junction because the injected majority carriers will appear as minority carriers in the n-type material.
Applying KCL to the transistor :
The collector current comprises of two components – the majority and minority carriers
ICO = IC current with emitter terminal open and is called leakage current.

## Slide 142: Different Region of OPERATION
Active
Region
Reverse
Active Region
Saturation Region
Cutoff Region
P
N
P
Collector
Emitter
Base
Forward
Reverse
VE
VC
VB
IE
IC
IB
P
N
P
Collector
Emitter
Base
Forward
VE
VC
VB
IE
IC
IB
Forward
P
N
P
Collector
Emitter
Base
Reverse
VE
VC
VB
Reverse
P
N
P
Collector
Emitter
Base
Reverse
Forward
VE
VC
VB
IE
IC
IB

## Slide 143: BJT CONFIGURATION
Output
B
E
C
Input
Common Emitter
Common Base
Common Collector
Output
B
E
C
Input
Input
E
B
C
Output

## Slide 144: COMMON-BASE CONFIGURATION
Common-base terminology is derived from the fact that the :
- base is common to both input and output of the configuration.
- base is usually the terminal closest to or at ground potential.
All current directions will refer to conventional (hole) flow and the arrows in all electronic symbols have a direction defined by this convention.
Note that the applied biasing (voltage sources) are such as to establish current in the direction indicated for each branch.

## Slide 145: COMMON-BASE CONFIGURATION
The free electrons which are flowing from emitter to base.
The holes which are flowing from base to emitter. The width of the base region is very thin. A small percentage of free electrons from emitter region will combine with the holes in the base region and the remaining large number of free electrons enters to the collector region.
Free electrons of the collector region will experience an attractive force and will flow towards the positive terminal of the battery. Thus, electric current is produced in the collector region.
VCB
VBE

## Slide 146: COMMON-BASE CONFIGURATION
To describe the behavior of common-base amplifiers requires two set of characteristics:
    Input or driving point characteristics.
    Output or collector characteristics
The output voltage VCB (collector-base voltage) is kept constant at zero volts and the input voltage VBE is increased from zero volts to different voltage levels.
Output voltage (VCB) is increased to 10 volts. Input voltage VBE is increased from 0 to different voltage levels.
When output voltage (VCB) is at 0 volts and emitter-base junction is forward biased, the emitter-base junction acts like a normal p-n junction diode. So the input characteristics are same as the forward characteristics of a normal pn junction diode. The cut in voltage of a silicon transistor is 0.7 volts.
When the output voltage (VCB) is increased to 10 volts, the emitter current flow will be increased (reduces the depletion region width at emitter-base junction). As a result, the turn on voltage will be reduced. Therefore, the curves shifted towards the left side for higher values of output voltage VCB.

## Slide 147: COMMON-BASE CONFIGURATION
The output characteristics has 3 basic regions:
    Active region – defined by the biasing arrangements
    Cutoff region – region where the collector current is 0A
    Saturation region- region of the characteristics to the left of VCB = 0V
Active Region: For a constant input current IE, when the output voltage VCB is increased, the output current IC remains constant.
Saturation region:
Both emitter-base junction and collector-base junction are forward biased.
A small increase in the collector voltage VCB there will be higher IC. Same as PN junction.
Cutoff region:
Both are Reverse biased and so flow of current.

## Slide 148: COMMON-BASE CONFIGURATION
VCB=0

## Slide 149: COMMON-BASE CONFIGURATION
ACTIVE REGION | SATURATION REGION | CUTOFF REGION
IE increased, IC increased |  | 
BE junction reverse biased and CB junction reverse biased | BE and CB junctions are forward biased | BE and CB junction are reverse biased
IC ≈ IE |  | No current flow at collector, only leakage current
IC does not depend on VCB | Small change in VCB will cause big difference in IC | 
Suitable region for the transistor to work as an amplifier | The allocation for this region is to the left of the VCB = 0 V | Region below the line of IE = 0

## Slide 150: COMMON-BASE CONFIGURATION
The curves (output characteristics) clearly indicate that a first approximation to the relationship between IE and IC in the active region is given by
IC ≈ IE
Once a transistor is in the ‘on’ state, the base-emitter voltage will be assumed to be
VBE = 0.7V
In the dc mode the level of IC and IE due to the majority carriers are related by a quantity called alpha

## Slide 151: COMMON-BASE CONFIGURATION
It can then be summarized to (ignore ICBO due to small value)
For ac situations where the point of operation moves on the characteristics curve, an ac alpha defined by
Alpha a common base current gain factor that shows the efficiency by calculating the current percent from current flow from emitter to collector. The value of is typical from 0.9 ~ 0.998.

## Slide 152
Thank You

## Slide 153
Electronic Devices
Reference book:
Electronic Devices and Circuit Theory (Chapter-3)
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Mid Term Lecture - 08
Faculty Name: Mr. A N M Shahebul Hasan
Email : shahebul@aiub.edu

## Slide 154
The proper biasing of the common-base configuration in the active region can be determined quickly using the approximation IC IE and assuming for the moment that IB 0 mA.
The result is the configuration of Fig. 3.11 for the pnp transistor.
For the npn transistor the polarities will be reversed.
BIASING

## Slide 155: COMMON-EMITTER CONFIGURATION
It is called common-emitter configuration since :
    emitter is common or reference to both input and output terminals.
    emitter is usually the terminal closest to or at ground potential.
Almost all amplifier design is using connection of CE due to the high gain for current and voltage.
Two set of characteristics are necessary to describe the behavior for CE:
    input (base terminal) and
    output (collector terminal) parameters.

## Slide 156: COMMON-EMITTER CONFIGURATION

## Slide 157: COMMON-EMITTER CONFIGURATION
VCE = VCB + VBE
VCB
VCE = VCB + VBE (Fixed)
VCB
VCB
VCB
IB
VCE = IB

## Slide 158: COMMON-EMITTER CONFIGURATION
IB is micro-amperes compared to milli-amperes of IC.
IB will flow when VBE > 0.7V for silicon and 0.3V for germanium
Before this value IB is very small.
Base-emitter junction is forward bias
Increasing VCE will reduce IB for different values.
Input characteristics for a
common-emitter n-p-n transistor
If VCE is increased, the depletion region width increases. The base region is lightly doped as compared to the collector region.
The width of the base region decreases which in turn reduces the input current (IB) produced in the base region.
Foe increasing VCE it will require
More VBE to turn on the region

## Slide 159: COMMON-EMITTER CONFIGURATION
For small VCE (VCE < VCESAT, IC increase linearly with increasing of VCE
IB(uA) is very small compare to IC (mA). Small increase in IB cause big increase in IC
IB=0 A  ICEO occur.
Noticing the value when IB=0A. There is still some value of current flows.
Output characteristics for a
common-emitter n-p-n transistor

## Slide 160: COMMON-EMITTER CONFIGURATION
ACTIVE REGION | SATURATION REGION | CUTOFF REGION
BE junction is forward biased | BE and CB junctions are forward biased, thus the values of IB and IC is too big | Region below IB = 0 µA is to be avoided if an undistorted output signal is required
CB junction is reverse biased | The value of VCE is too small | BE junction and CB junctions are reverse biased
Can e employed for voltage, current and power amplification | Suitable region when the transistor is used a logic switch | IB = 0, IC not zero, during this condition IC = ICEO where this is the current flow when BE is reverse biased
 | NOT and avoid this region when the transistor as an amplifier | 

## Slide 161: BETA (β) OR AMPLIFICATION FACTOR
The ratio of dc collector current (IC) to the dc base current (IB) is dc beta (βdc ) which is dc current gain where IC and IB are determined at a particular operating point, Q-point (quiescent point).
It’s defined by the following equation:
For ac conditions an ac beta has been defined as the changes of collector current (IC) compared to the changes of base current (IB) where IC and IB are determined at operating point.
It can be defined by the following equation:

## Slide 162: RELATIONSHIP ANALYSIS BETWEEN α AND β

## Slide 163: COMMON–COLLECTOR CONFIGURATION
Also called emitter-follower (EF).
It is called common-emitter configuration since both the signal source and the load share the collector terminal as a common connection point.
The output voltage is obtained at emitter terminal.
The input characteristic of common-collector configuration is similar with common-emitter configuration.
Common-collector circuit configuration is provided with the load resistor connected from emitter to ground.
It is used primarily for impedance-matching purpose since it has high input impedance and low output impedance.

## Slide 164: COMMON–COLLECTOR CONFIGURATION

## Slide 165: LIMITS OF OPERATION
Many BJT transistor used as an amplifier. Thus it is important to notice the limits of operations.
At least 3 maximum values is mentioned in data sheet.
There are:
    Maximum power dissipation at collector: PCmax or PD
    Maximum collector-emitter voltage: VCEmax ;sometimes named as V(BR)CEO) or VCEO.
    Maximum collector current: Icmax
There are few rules that need to be followed for BJT transistor used as an amplifier. The rules are:
    transistors need to operate in active region!
    IC < Icmax
    PC < PCmax

## Slide 166: LIMITS OF OPERATION
Note: VCE is at maximum and IC is at minimum (ICmax=ICEO) in the cutoff region. IC is at maximum and VCE is at minimum (VCE max = VCEsat = VCEO) in the saturation region. The transistor operates in the active region between saturation and cutoff

## Slide 167
Thank You

## Slide 168
Electronic Devices
Reference book:
Electronic Devices and Circuit Theory (Chapter-4)
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Mid Term Lecture - 09
Faculty Name: Dr. Mohammad Alif Arman
Email : dr.alifarman@aiub.edu
Room: DN0526

## Slide 169
Be able to determine the dc levels for the variety of important BJT configurations.
Understand how to measure the important voltage levels of a BJT transistor configuration and use them to determine whether the network is operating properly.
Become aware of the saturation and cutoff conditions of a BJT network and the expected voltage and current levels established by each condition.
Be able to perform a load-line analysis of the most common BJT configurations.
Become acquainted with the design process for BJT amplifiers.
Understand the basic operation of transistor switching networks.
Begin to understand the troubleshooting process as applied to BJT configurations.
Develop a sense for the stability factors of a BJT configuration and how they affect its operation due to changes in specific characteristics and environmental changes.
Objectives

## Slide 170: BIASING
Applying DC voltages to the transistor to turn it on so that it can amplify AC signal.
Once the desired DC current and voltage levels have been defined, a network must be constructed that will establish the desired operating point.

## Slide 171: INTRODUCTION
BJT amplifier design requires knowledge of both the DC and AC.
BJT needs to be operated in active region used as amplifier.
BJT operated in cut-off and saturation region is used as a switch.
The following basic current relationships for a transistor are required for transistor network analysis:
VBE = 0.7 V
IE = (β+1) IB IC
IC = β IB

## Slide 172: INTRODUCTION
Biasing:
Applying DC voltages to establish a fixed level of current and voltage.
The applied DC establishes an operating point (Q-point) that define the region for the signal amplification.
For a BJT to be biased in active operating region, the following must be true:
        BE junction = forward biased
        BC junction = reverse biased

## Slide 173: BIASING AND THE 3 STATES OF OPERATION

## Slide 174: OPERATING POINT (Q-POINT)
Operating Point: Quiescent point or Q-point (static point)
The biasing circuit can be designed to set the device operation at any of these points or others within the active region.
The BJT device could be biased to operate outside the max limits, but the result of such operation would be shortening of the lifetime of the device or destruction of the device.
The chosen Q-point often depends on the intended use of the circuit.

## Slide 175: VARIOUS Q-POINTS WITHIN THE LIMITS OF OPERATION

## Slide 176: BJT BIAS CONFIGURATIONS
Fixed-Bias Configuration
Emitter-Bias Configuration
Voltage-Divider Bias Configuration
Collector Feedback Configuration

## Slide 177: FIXED-BIAS CONFIGURATION

## Slide 178: FORWARD BIAS OF BASE–EMITTER

## Slide 179: COLLECTOR–EMITTER LOOP

## Slide 180: FIXED-BIAS CONFIGURATION EXAMPLE

## Slide 181: Transistor Saturation
For a transistor operating in the saturation region, the current is a maximum value for the particular design
The highest saturation level is defined by the maximum collector current as provided by the specification sheet.
Saturation conditions are normally avoided because the base–collector junction is no longer reverse-biased and the output amplified signal will be distorted.
It is in a region where the characteristic curves join, and the collector-to-emitter voltage is at or below .
The resulting saturation current for the fixed-bias configuration is
See Example 4.2

## Slide 182: Load-Line Analysis
The characteristics of the BJT are superimposed on a plot of the network equation defined by the same axis parameters
The load resistor for the fixed-bias configuration will define the slope of the network equation and the resulting intersection between the two plots.
The network of Fig. 4.11(a) establishes an output equation that relates the variables and in the following manner:

## Slide 183: Load-Line Analysis

## Slide 184: EXAMPLE

## Slide 185
Thank You

## Slide 186
Electronic Devices
Reference book:
Electronic Devices and Circuit Theory (Chapter-4)
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Mid Term Lecture - 10
Faculty Name: Dr. Mohammad Alif Arman
Email : dr.alifarman@aiub.edu
Room: DN0526

## Slide 187
Objectives
Be able to determine the dc levels for the variety of important BJT configurations.
Understand how to measure the important voltage levels of a BJT transistor configuration and use them to determine whether the network is operating properly.
Become aware of the saturation and cutoff conditions of a BJT network and the expected voltage and current levels established by each condition.
Be able to perform a load-line analysis of the most common BJT configurations.
Become acquainted with the design process for BJT amplifiers.
Understand the basic operation of transistor switching networks.
Begin to understand the troubleshooting process as applied to BJT configurations.
Develop a sense for the stability factors of a BJT configuration and how they affect its operation due to changes in specific characteristics and environmental changes.

## Slide 188: EMITTER-BIAS CONFIGURATION

## Slide 189: BIAS STABILITY
If VBE is held constant and the temperature rises, the current through the base-emitter diode IB will increase, and thus the collector IC will also increase. The power dissipated in the transistor may also increase, which will further increase its temperature and exacerbate the problem. This deleterious positive feedback results in thermal runaway.
Adding RE to the Emitter improves the stability of a transistor.
Stability refers to a bias circuit in which the currents and voltages will remain fairly constant for a while range of temperatures and transistor Beta’s (β).
VRB = VCC – IERE – VBE

## Slide 190
If temperature increases, emitter current increases.
However, a larger IE increases the emitter voltage VE =IERE, which in turn reduces the voltage VRB across the base resistor.
A lower base-resistor voltage drop reduces the base current, which results in less collector current because IC = βIB.
BIAS STABILITY

## Slide 191: BASE–EMITTER LOOP

## Slide 192
BASE–EMITTER LOOP

## Slide 193: COLLECTOR–EMITTER LOOP

## Slide 194: EXAMPLE

## Slide 195: EXAMPLE

## Slide 196: VOLTAGE-DIVIDER BIAS CONFIGURATION
The bias current and voltage is a function of the current gain β of the transistor
Since β is temperature sensitive, especially for silicon transistors, it would be desirable to develop a bias circuit that is independent of, the transistor β.
The voltage-divider bias configuration is such a network.

## Slide 197: EXACT ANALYSIS

## Slide 198: EXAMPLE

## Slide 199: EXAMPLE CONTD.

## Slide 200: Approximate Analysis

## Slide 201: EXAMPLE

## Slide 202: COLLECTOR FEEDBACK CONFIGURATION
An improved level of stability can also be obtained by introducing a feedback path from collector to base
Although the Q-point is not totally independent of beta (even under approximate conditions), the sensitivity to changes in beta or temperature variations is normally less than encountered for the fixed-bias or emitter-biased configurations.
The analysis will again be performed by first analyzing the base–emitter loop, with the results then applied to the collector–emitter loop

## Slide 203: BASE–EMITTER LOOP

## Slide 204: COLLECTOR–EMITTER LOOP

## Slide 205
Thank You