## Slide 1
Electronic Devices
Reference book:
Electronic Devices and Circuit Theory (Chapter-5)
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Final Term Lecture - 01

## Slide 2: OBJECTIVES
Become familiar with there, re, hybrid and hybrid pi models for the BJT transistor.
Learn to use the equivalent model to find the important ac parameters for an amplifier.
Understand the effects of a source resistance and load resistor on the overall gain and characteristics of an amplifier.
Become aware of the general ac characteristics of a variety of important BJT configurations.
Begin to understand the advantages associated with the two-port systems approach to single- and multistage amplifiers.
Develop some skill in troubleshooting ac amplifier networks.

## Slide 3: BJT TRANSISTOR MODELING
A model is an equivalent circuit that represents the AC characteristics of the transistor.
A model uses circuit elements that approximate the behavior of the transistor.
There are two models commonly used in small signal AC analysis of a transistor:
    re model
    Hybrid equivalent model

## Slide 4: BJT TRANSISTOR MODELING
Capacitors chosen with very small reactance at the frequency of application → replaced by low-resistance or short circuit.
Removal of the dc supply and insertion of the short-circuit equivalent for the capacitors.

## Slide 5: BJT TRANSISTOR MODELING
Circuit redrawn for small signal ac analysis

## Slide 6: The re Transistor Model (Common Emitter Configuration)

## Slide 7: The re Transistor Model (Common Emitter Configuration)

## Slide 8: The re Transistor Model (Common Emitter Configuration)

## Slide 9: The re Transistor Model (Common Emitter Configuration)
The Early effect, named after its discoverer James M. Early, is the variation in the effective width of the base in a bipolar junction transistor (BJT) due to a variation in the applied base-to-collector voltage.
A greater reverse bias across the collector–base junction, for example, increases the collector–base depletion width, thereby decreasing the width of the charge carrier portion of the base.

## Slide 10: COMMON-BASE CONFIGURATION

## Slide 11: COMMON-BASE CONFIGURATION
Common Base re equivalent circuit
The output resistance r0 is quite high. typically extend into the MΩ range.

## Slide 12: COMMON EMITTER FIXED BIAS CONFIGURATION

## Slide 13: COMMON EMITTER FIXED BIAS CONFIGURATION

## Slide 14: COMMON EMITTER FIXED BIAS CONFIGURATION
INPUT IMPEDANCE, Zi
β
β|
OUTPUT IMPEDANCE, Zo
|
VOLTAGE GAIN, Av
)
= - , = -
For the majority of situations R B is greater than b r e by more than a factor of 10

## Slide 15: COMMON EMITTER FIXED BIAS PHASE RELATIONSHIP
= -
Demonstrating the 180° phase shift between input and output waveforms.
Why is transistor output inverted?
The inversion is because of the direction of the current source is the reverse of the vbe, so an increase in vbe results in decrease of vce

## Slide 16: EXAMPLE
EXAMPLE 5.1: For the network of Fig. 5.25 :
Determine re, Zi (with ro = ∞), Zo (with ro = ∞), Av (with ro = ∞) and Repeat with ro = 50 kΩ.

## Slide 17
End of Lecture-1

## Slide 18: COMMON-EMITTER VOLTAGE-DIVIDER BIAS

## Slide 19: COMMON-EMITTER VOLTAGE-DIVIDER BIAS
INPUT IMPEDANCE, Zi
β
OUTPUT IMPEDANCE, Zo
|
VOLTAGE GAIN, Av
)
= - , = -

## Slide 20: EXAMPLE
EXAMPLE 5.2: For the network of Fig. 5.28 :
Determine re, Zi, Zo (with ro = ∞), Av (with ro = ∞) and Repeat with ro = 50 kΩ.

## Slide 21: EXAMPLE Contd.

## Slide 22: COMMON-EMITTER EMITTER-BIAS CONFIGURATION: UNBYPASSED RE

## Slide 23: IMPEDANCE CALCULATION
INPUT IMPEDANCE, Zi
=
OUTPUT IMPEDANCE, Zo

## Slide 24: GAIN CALCULATIONS
VOLTAGE GAIN, Av
= ()
= -
= -
= -
The negative sign in gain equations reveals 180° phase shift between input and output waveforms.

## Slide 25: COMMON-EMITTER EMITTER-BIAS CONFIGURATION: BYPASSED RE
Bypassed
If RE is bypassed by an emitter capacitor CE, the complete re equivalent model can be substituted, resulting in the same equivalent network as Fig. 5.22. Equations of slide no. 13 are therefore applicable.

## Slide 26: EXAMPLE
EXAMPLE 5.3: For the network of following Fig, without CE (unbypassed), determine: re, Zi, Zo & Av.

## Slide 27: EXAMPLE Contd.

## Slide 28: EMITTER-FOLLOWER CONFIGURATION
This is also known as the common-collector configuration.
The input is applied to the base and the output is taken from the emitter.
There is no phase shift between input and output.

## Slide 29: IMPEDANCE CALCULATIONS
INPUT IMPEDANCE, Zi

## Slide 30: IMPEDANCE CALCULATIONS
OUTPUT IMPEDANCE, Zo
= || = |

## Slide 31: GAIN CALCULATIONS
VOLTAGE GAIN, Av
and
See Example 5.7

## Slide 32: COMMON-BASE CONFIGURATION
The input is applied to the emitter.
The output is taken from the collector.
Low input impedance.
High output impedance.
Very high voltage gain.
No phase shift between input and output.

## Slide 33: CALCULATIONS
INPUT IMPEDANCE, Zi
OUTPUT IMPEDANCE, Zo
VOLTAGE GAIN, Av
;
=
;
CURRENT GAIN, Ai

## Slide 34: COMMON-BASE CONFIGURATION
Phase Relationship:
The fact that Av is a positive number shows that Vo and Vi are in phase for the common-base configuration.
Effect of ro :
For the common-base configuration, ro = 1/hob is typically in the megohm range and sufficiently larger than the parallel resistance RC to permit the approximation ro || RC RC.

## Slide 35: EXAMPLE
EXAMPLE 5.8: For the network of following figure, determine: re, Zi, Zo, Av, Ai.

## Slide 36
End of Lecture-2

## Slide 37: FETs vs BJTs
FET’s (Field – Effect Transistors) are much like BJT’s (Bipolar Junction Transistors).
Similarities:
    Amplifiers
    Switching devices
    Impedance matching circuits
Differences:
    FET’s are voltage controlled devices whereas BJT’s are current controlled devices.
    FET’s are unipolar devices whereas BJT’s are bipolar devices.
    FET’s also have a higher input impedance, but BJT’s have higher gains.
    FET’s are less sensitive to temperature variations and because of their construction they are more easily integrated into IC’s.

## Slide 38: FET TYPES
JFET: Junction Field-Effect Transistor
MOSFET: Metal-Oxide Semiconductor Field-Effect Transistor
        D-MOSFET ~ Depletion type MOSFET
        E-MOSFET ~ Enhancement type MOSFET

## Slide 39: JFET CONSTRUCTION
There are two types of JFETs
    n- channel
    p- channel
The n-channel is more widely used.
There are three terminals:
    Drain (D) and Source (S) are connected to n-channel
    Gate (G) is connected to the p-type material
Check this: http://www-g.eng.cam.ac.uk/mmg/teaching/linearcircuits/jfet.html

## Slide 40: BASIC OPERATION OF JFET
JFET operation can be compared to a water spigot.
The source of water pressure is the accumulation of electrons at the negative pole of the drain-source voltage.
The drain of the water is the electron deficiency (or holes) at the positive pole of the applied voltage.
The control of flow of water is the gate voltage that controls the width of the n channel and therefore, the flow of charges from source to drain.

## Slide 41: JFET OPERATING CHARACTERISTICS
There are three basic operating conditions for a JFET:
A. VGS = 0, VDS increasing to some positive value
B. VGS < 0, VDS at some positive value
C. Voltage-Controlled Resistor

## Slide 42: JFET OPERATING CHARACTERISTICS: VGS = 0 V
Three things happen when VGS = 0 and VDS is increased from 0 to a more positive voltage:
    The depletion region between p-gate and n-channel increases as electrons from n-channel combine with holes from p-gate.
    Increasing the depletion region, decreases the size of the n-channel which increases the resistance of the n-channel.
    But even though the n-channel resistance is increasing, the current (ID) from Source to Drain through the n-channel is increasing. This is because VDS is increasing.

## Slide 43: JFET OPERATING CHARACTERISTICS: VGS = 0 V
It is important to note that the depletion region is wider near the top of both p-type Materials.
Assuming a uniform resistance in the n-channel, the resistance of the channel can be broken down to the divisions appearing in Figure.
The current ID will establish the voltage levels through the channel as indicated on the same figure. The result is that the upper region of the p-type material will be reverse biased by about 1.5 V, with the lower region only reverse-biased by 0.5 V.
The greater the applied reverse bias, the wider the depletion region—hence the distribution of the depletion region as shown in figure. The fact that the p-n junction is reverse-biased for the length of the channel results in a gate current of zero amperes.

## Slide 44: PINCH-OFF
If VGS = 0 and VDS is further increased to a more positive voltage, then the depletion zone gets so large that it pinches off the n-channel.
This suggests that the current in the n-channel (ID) would drop to 0A, but it does just the opposite: as VDS increases, so does ID.

## Slide 45: SATURATION
At the pinch-off point:
Any further increase in VDS does not produce any increase in ID. VDS at pinch-off is denoted as Vp.
ID is at saturation or maximum. It is referred to as IDSS.
The ohmic value of the channel is at maximum.

## Slide 46: ID < IDSS
As VGS becomes more negative:
The JFET will pinch-off at a lower value of VDS.
ID decreases (ID < IDSS) even though VDS is increased.
Eventually ID will reach 0A. VGS at this point is called Vp or VGS(off).
Also note that at high levels of VDS the JFET reaches a breakdown situation. ID will increases uncontrollably if VDS > VDSmax.

## Slide 47: JFET OPERATING CHARACTERISTICS: VOLTAGE CONTROLLED RESISTOR
The region to the left of the pinch-off point is called the ohmic region.
The JFET can be used as a variable resistor, where VGS controls the drain-source resistance (rd).
The slope of each curve and therefore the resistance of the device between drain and source for VDS < VP is a function of the applied voltage VGS.
As VGS becomes more negative, the resistance (rd) increases.

## Slide 48: P-CHANNEL JFETS
p-Channel JFET acts the same as the n-channel JFET, except the polarities and currents are reversed.

## Slide 49
Electronic Devices
Reference book:
Electronic Devices and Circuit Theory (Chapter-6)
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Final Term Lecture - 04

## Slide 50: P-CHANNEL JFET CHARACTERISTICS
As VGS increases more positively:
    The depletion zone increases
    ID decreases (ID < IDSS)
    Eventually ID = 0A
Also note that at high levels of VDS the JFET reaches a breakdown situation. ID increases uncontrollably if VDS > VDSmax.

## Slide 51: JFET SYMBOLS

## Slide 52: SUMMARY TILL NOW
The maximum current is defined as IDSS and occurs when VGS = 0 V and VDS ≥ |Vp|, as shown in Fig. 6.15a .
For gate-to-source voltages VGS is less than (more negative than) the pinch-off level, the drain current is 0 A (ID = 0 A ), as in Fig. 6.15b .
For all levels of VGS between 0 V and the pinch-off level, the current ID will range between IDSS and 0 A, respectively, as in Fig. 6.15c.
A similar list can be developed for p-channel JFETs.

## Slide 53: SUMMARY TILL NOW

## Slide 54: JFET TRANSFER CHARACTERISTICS
The transfer characteristic of input-to-output is not as straight forward in a JFET as it was in a BJT.
In a BJT,  indicated the relationship between IB (input) and IC (output).
In a JFET, the relationship of VGS (input) and ID (output) is a little more complicated (Shockley’s equation):

## Slide 55: TRANSFER CURVE

## Slide 56: PLOTTING THE TRANSFER CURVE
Using IDSS and Vp (VGS(off)) values found in a specification sheet, the Transfer Curve can be plotted using these 3 steps:
Step 1:
Solving for VGS = 0V:
Step 2:
Solving for VGS = Vp (VGS(off)):
Step 3:
Solving for VGS = 0V to Vp:

## Slide 57: SHORTHAND METHOD
VGS | ID
0 | IDSS
0.3VP | IDSS/2
0.5VP | IDSS/4
VP | 0mA
When VGS = 0 V, ID = IDSS
When VGS = VP, ID = 0 mA

## Slide 58: EXAMPLE

## Slide 59: EXAMPLE

## Slide 60: MOSFETs
MOSFETs have characteristics similar to JFETs and additional characteristics that make them very useful.
There are 2 types:
    Depletion-Type MOSFET
    Enhancement-Type MOSFET

## Slide 61: ENHANCEMENT-TYPE MOSFET CONSTRUCTION
The Drain (D) and Source (S) connect to the to n-doped regions.
The Gate (G) connects to the p-doped substrate via a thin insulating layer of SiO2.
There is no channel. The n-doped material lies on a p-doped substrate that may have an additional terminal connection called SS.
In summary, therefore, the construction of an enhancement-type MOSFET is quite similar to that of the depletion-type MOSFET, except for the absence of a channel between the drain and source terminals.

## Slide 62: CONTINUED…
As VGS increases in magnitude, the concentration of electrons near the SiO2 surface increases until eventually the induced n-type region can support a measurable flow between drain and source.
The level of VGS that results in the significant increase in drain current is called the threshold voltage and is given the symbol VT.
Since the channel is nonexistent with VGS=0 V and “enhanced” by the application of a positive gate-to-source voltage, this type of MOSFET is called an enhancement-type MOSFET.

## Slide 63: CONTINUED…
As VGS is increased beyond the threshold level, the density of free carriers in the induced channel will increase, resulting in an increased level of drain current.
However, if we hold VGS constant and increase the level of VDS, the drain current will eventually reach a saturation level The levelling off of ID is due to a pinching-off process depicted by the narrower channel at the drain end of the induced channel.
By applying KVL we get –
If VGS is held fixed at some value such as 8 V and VDS is increased from 2 to 5V, the voltage will drop from -6 to -3 V. This reduction in gate-to-drain voltage will in turn reduce the attractive forces for free carriers (electrons) in this region of the induced channel, causing a reduction in the effective channel width.
Eventually, the channel will be reduced to the point of pinch-off and a saturation condition will be established.

## Slide 64: CONTINUED…

## Slide 65: BASIC OPERATION
The Enhancement-type MOSFET only operates in the enhancement mode.
VGS is always positive.
As VGS increases, ID increases.
But if VGS is kept constant and VDS is increased, then ID saturates (IDSS).
The saturation level, VDSsat is reached.
Check this: http://www-g.eng.cam.ac.uk/mmg/teaching/linearcircuits/jfet.html

## Slide 66
End of Lecture-4

## Slide 67: TRANSFER CURVE
To determine ID given VGS:
where VT = threshold voltage or voltage at which the MOSFET turns on.
k = constant found in the specification sheet
k can also be determined by using values at a specific point and the formula:
VDSsat can also be calculated:

## Slide 68: P -CHANNEL ENHANCEMENT-TYPE MOSFETS
The p-channel Enhancement-type MOSFET is similar to the n-channel except that the voltage polarities and current directions are reversed.

## Slide 69: SYMBOLS

## Slide 70: DEPLETION-TYPE MOSFET CONSTRUCTION
The Drain (D) and Source (S) connect to the to n-doped regions.
These N-doped regions are connected via an n-channel. This n-channel is connected to the Gate (G) via a thin insulating layer of SiO2.
The n-doped material lies on a p-doped substrate that may have an additional terminal connection called SS.

## Slide 71: BASIC OPERATION
In Fig. 6.25 the gate-to-source voltage is set to 0 V by the direct connection from one terminal to the other, and a voltage VDD is applied across the drain-to-source terminals.
The result is an attraction of the free electrons of the n-channel for the positive voltage at the drain.
The result is a current similar to that flowing in the channel of the JFET. In fact, the resulting current with VGS = 0 V continues to be labeled IDSS.

## Slide 72: BASIC OPERATION
A Depletion MOSFET can operate in two modes: Depletion or Enhancement mode.

## Slide 73: BASIC OPERATION CONTD.
In this figure VGS has been set at a negative voltage such as 1 V. The negative potential at the gate will tend to pressure electrons toward the p-type substrate (like charges repel) and attract holes from the p-type substrate (opposite charges attract).
Depending on the magnitude of the negative bias established by VGS, a level of recombination between electrons and holes will occur that will reduce the number of free electrons in the n-channel available for conduction. The more negative the bias, the higher the rate of recombination.
The resulting level of drain current is therefore reduced with increasing negative bias for VGS for VGS =1 V, 2 V, and so on, to the pinch-off level of 6 V. The resulting levels of drain current and the plotting of the transfer curve proceeds exactly as described for the JFET.

## Slide 74: DEPLETION-TYPE MOSFET IN DEPLETION MODE
Depletion mode:
The characteristics are similar to the JFET.
When VGS = 0V, ID = IDSS
When VGS < 0V, ID < IDSS
The formula used to plot the Transfer Curve still applies:

## Slide 75: ENHANCEMENT MODE
For positive values of VGS, the positive gate will draw additional electrons (free carriers) from the p-type substrate due to the reverse leakage current and establish new carriers through the collisions resulting between accelerating particles.
As the gate-to-source voltage continues to increase in the positive direction, the drain current will increase at a rapid rate.
The application of a positive gate-to-source voltage has “enhanced” the level of free carriers in the channel compared to that encountered with VGS =0 V. For this reason the region of positive gate voltages on the drain or transfer characteristics is often referred to as the enhancement region,
The region between cutoff and the saturation level of IDSS referred to as the depletion region.

## Slide 76: DEPLETION-TYPE MOSFET IN ENHANCEMENT MODE
Enhancement mode:
VGS > 0V, ID increases above IDSS.
The formula used to plot the Transfer Curve still applies:
(note that VGS is now a positive polarity)

## Slide 77: P-CHANNEL DEPLETION-TYPE MOSFET
The p-channel Depletion-type MOSFET is similar to the n-channel except that the voltage polarities and current directions are reversed.

## Slide 78: SYMBOLS

## Slide 79: SUMMARY TABLE

## Slide 80: MOSFET HANDLING
MOSFETs are very static sensitive. Because of the very thin SiO2 layer between the external terminals and the layers of the device, any small electrical discharge can stablish an unwanted conduction.
Protection:
    Always transport in a static sensitive bag.
    Always wear a static strap when handling MOSFETS.
    Apply voltage limiting devices between the Gate and Source, such as back-to-back Zeners to limit any transient voltage.

## Slide 81: CMOS
CMOS – Complementary MOSFET p-channel and n-channel MOSFET on the same substrate.
Advantage:
    Useful in logic circuit designs
    Higher input impedance
    Faster switching speeds
    Lower operating power levels
Application:
    CMOS Inverter

## Slide 82: CMOS INVERTER
An inverter is a logic element that “inverts” the applied signal. That is, if the logic levels of operation are 0V (0-state) and 5V (1-state), an input level of 0V will result in an output level of 5V, and vice versa.
Here, both gates are connected to the applied signal and both drain to the output Vo. The source of the p-channel MOSFET (Q2) is connected directly to the applied voltage VSS, while the source of the n-channel MOSFET (Q1) is connected to ground.
Here, the application of 5V at the input should result in approximately 0 V at the output. With 5V at Vi (with respect to ground), VGS1 = Vi and Q1 is “on,” resulting in a relatively low resistance between drain and source.
Since Vi and VSS are at 5 V, VGS2 = 0 V, which is less than the required VT for the device, resulting in an “off” state. The resulting resistance level between drain and source is quite high for Q2.

## Slide 83: CMOS INVERTER
A simple application of the voltage-divider rule will reveal that Vo is very close to 0 V or the 0-state, establishing the desired inversion process.
For an applied voltage Vi of 0V (0-state), VGS1 = 0V and Q1 will be off with VSS2 =-5V, turning on the p-channel MOSFET. The result is that Q2 will present a small resistance level, Q1 a high resistance, and Vo =VSS =5 V (the 1-state).

## Slide 84
End of Lecture-5

## Slide 85: OBJECTIVES
Be able to perform a dc analysis of JFET, MOSFET, and MESFET networks.
Become proficient in the use of load-line analysis to examine FET networks.
Develop confidence in the dc analysis of networks with both FETs and BJTs.
Understand how to use the Universal JFET Bias Curve to analyze the various FET configurations.

## Slide 86: GENERAL RELATIONSHIPS
For all FETs:
For JFETs and Depletion-Type MOSFETs:
For Enhancement-Type MOSFETs:
BJT: Linear Relationship between IB and IC
FET: Non-linear Relationship between VGS and ID.

## Slide 87: COMMON FET BIASING CIRCUITS
JFET
    Fixed – Bias
    Self-Bias
    Voltage-Divider Bias
Depletion-Type MOSFET
    Self-Bias
    Voltage-Divider Bias
Enhancement-Type MOSFET
    Feedback Configuration
    Voltage-Divider Bias

## Slide 88: FIXED-BIAS JFET
The simplest biasing arrangements:
For the DC analysis,
    Capacitors are open circuits
The zero-volt drop across RG permits replacing RG by a short-circuit.

## Slide 89: FIXED-BIAS JFET
Can be solved using either Mathematical Approach or Graphical Approach:
Mathematical Approach
Graphical Approach

## Slide 90: FIXED-BIAS JFET EXAMPLE
Determine VGSQ, IDQ, VDS, VD, VG, VS.

## Slide 91: FIXED-BIAS JFET EXAMPLE
Graphical Approach
VGS | ID
0 | IDSS
0.3VP | IDSS/2
0.5VP | IDSS/4
VP | 0mA

## Slide 92: JFET: SELF-BIAS CONFIGURATION
The self-bias configuration eliminates the need for two dc supplies.

## Slide 93: SELF-BIAS CONFIGURATION
Can be solved using either Mathematical Approach or Graphical Approach:

## Slide 94: SELF-BIAS CONFIGURATION
Draw the device transfer characteristic using shorthand method.
Draw the network load line
    Use to draw straight line.
    First point,
    Second point, any point from ID = 0 to ID = IDSS. Choose
The Q-point obtained at the intersection of the straight line plot and the device characteristic curve.
The quiescent value for ID and VGS can then be determined and used to find the other quantities of interest.
Graphical Approach

## Slide 95: SELF-BIAS CONFIGURATION

## Slide 96: SELF-BIAS EXAMPLE
Determine VGSQ, IDQ,VDS,VS,VG and VD.

## Slide 97: SELF-BIAS EXAMPLE Contd.
Plot ID vs VGS and draw a line from the origin of the axis.

## Slide 98
End of Lecture-6

## Slide 99: SELF-BIAS EXAMPLE Contd.
Plot the transfer curve using IDSS and VP using shorthand method:
VGS | ID
0 | IDSS
0.3VP | IDSS/2
0.5VP | IDSS/4
VP | 0mA

## Slide 100: SELF-BIAS EXAMPLE Contd.
Superimpose the load line on top of the transfer curve:

## Slide 101: JFET: VOLTAGE-DIVIDER BIAS
The source VDD was separated into two equivalent sources to permit a further separation of the input and output regions of the network.
Since IG = 0A, Kirchoff’s current law requires that IR1= IR2 and the series equivalent circuit appearing to the left of the figure can be used to find the level of VG.

## Slide 102: VOLTAGE-DIVIDER BIAS
VG can be found using the voltage divider rule:
Using Kirchoff’s Law on the input loop:
Rearranging and using ID =IS:
Again the Q point needs to be established by plotting a line that intersects the transfer curve.

## Slide 103: VOLTAGE-DIVIDER BIAS
Graphical Approach ( to find VGSQ and IDQ):
    Plot a line for:
        VGS = VG when ID = 0A
        VGS = 0V when ID = VG/RS.
    Plot the transfer curve using IDSS and VP using shorthand method.
    The Q-point is located at the intersection.
VGS | ID
0 | IDSS
0.3VP | IDSS/2
0.5VP | IDSS/4
VP | 0mA

## Slide 104: EFFECT OF INCREASING VALUES OF RS

## Slide 105
Determine IDQ, VGSQ, VD, VS, VDS and VDG.
JFET: VOLTAGE-DIVIDER BIAS EXAMPLE

## Slide 106
Graphical Approach ( to find VGSQ and IDQ):
    Plot a line for:
        VGS = VG when ID = 0A
        VGS = 0V when ID = VG/RS.
    Plot the transfer curve using IDSS and VP using shorthand method.
    Identify the Q-point.
VOLTAGE-DIVIDER BIAS EXAMPLE Contd.

## Slide 107: D-MOSFET SELF-BIAS
D-MOSFET bias circuits are similar to JFETs.
The only difference is that D-MOSFETs can operate with positive values of VGS and with ID values that exceed IDSS.

## Slide 108: D-MOSFET SELF-BIAS
Graphical Approach (to find VGSQ and IDQ):
    Plot the transfer curve using IDSS and VP using shorthand method.
    Plot ID vs VGS using VGS = -IDRS.
    Take a positive value of VGS and find the ID value using
    The Q-point is located at the intersection.

## Slide 109: D-MOSFET SELF-BIAS EXAMPLE
Determine the IDQ, VGSQ and VD.
Graphical Approach (to find VGSQ and IDQ):
    Plot the transfer curve using IDSS and VP using shorthand method.
    Take a positive value of VGS and find the ID value using
    Plot ID vs VGS using VGS = -IDRS.
    Identify the intersection Q-point.

## Slide 110: D-MOSFET SELF-BIAS EXAMPLE
VGSQ = -4.3 V
IDQ = 1.7 mA
VD = 9.46 V

## Slide 111: D-MOSFET VOLTAGE-DIVIDER BIAS
D-MOSFET bias circuits are similar to JFETs.

## Slide 112: D-MOSFET VOLTAGE-DIVIDER BIAS
Graphical Approach (to find VGSQ and IDQ):
    Plot the transfer curve using IDSS and VP using shorthand method.
    Take a positive value of VGS and find the ID value using
    Plot ID vs VGS using VGS = VG - IDRS.
    The Q-point is located at the intersection.

## Slide 113
End of Lecture-7

## Slide 114
E-MOSFET VOLTAGE-DIVIDER BIAS
E-MOSFETs use the same procedure to JFETs and D-MOSFETs.

## Slide 115: E-MOSFET VOLTAGE-DIVIDER BIAS
Graphical Approach:
    Calculate the value for
    Plot VGS vs ID using
    Plot for:
        VGS = VG at ID = 0A
        VGS = 0V at ID = VG/RS
    Identify the Q-point.

## Slide 116: E-MOSFET VOLTAGE-DIVIDER BIAS EXAMPLE
Determine ID, VGS, and VDS for the following network:

## Slide 117: E-MOSFET VOLTAGE-DIVIDER BIAS EXAMPLE

## Slide 118: E-MOSFET FEEDBACK BIAS

## Slide 119: E-MOSFET FEEDBACK BIAS
Graphical Approach (to find VGSQ and IDQ):
    Calculate the value for
    Plot VGS vs ID for the range of interest.
    Plot :
    Identify the Q-point.

## Slide 120: E-MOSFET FEEDBACK BIAS EXAMPLE
Example 7.10: Determine IDQ and VDSQ for the following circuit:

## Slide 121: E-MOSFET FEEDBACK BIAS EXAMPLE CONTD.

## Slide 122: E-MOSFET FEEDBACK BIAS EXAMPLE CONTD.

## Slide 123: p-CHANNEL FETs
For p-channel FETs the same calculations and graphs are used, except that the voltage polarities and current directions are the opposite.
The graphs will be mirrors of the n-channel graphs.

## Slide 124
End of Lecture-8

## Slide 125: OBJECTIVES
Become acquainted with the small-signal ac model for a JFET and MOSFET.
Be able to perform a small-signal ac analysis of a variety of JFET and MOSFET configurations.
Begin to appreciate the design sequence applied to FET configurations.
Understand the effects of a source resistor and load resistor on the input impedance, output impedance and overall gain.
Be able to analyze cascaded configurations with FETs and/or BJT amplifiers.

## Slide 126: Introduction
Field-effect transistor amplifiers provide an excellent voltage gain with the added feature of a high input impedance.
JFET Small-Signal Model
The ac analysis of a JFET Configuration requires that a small-signal ac model for the JFET be developed.
The gate-to-source voltage controls the drain-to-source (channel) current of a JFET.
The change in drain current that will result from a change in gate-to-source voltage can be determined using the transconductance factor gm in the following manner:

## Slide 127: Graphical Determination of gm

## Slide 128: Example:

## Slide 129
Mathematical Definition of gm
The derivative of a function at a point is equal to the slope of the tangent line drawn at that point.

## Slide 130: Example

## Slide 131: Plotting gm versus VGS

## Slide 132: Example

## Slide 133: Effect of ID on gm

## Slide 134: Example

## Slide 135
End of Lecture-9

## Slide 136
JFET Small Signal Model

## Slide 137: JFET AC Equivalent Circuit

## Slide 138: Example

## Slide 139: FIXED-BIAS CONFIGURATION

## Slide 140: Continued.

## Slide 145
End of Lecture-10